## Slide 1: EECS 498 Advanced Embedded Systems
Lecture 9:
Batteries and DC converters

## Slide 2: Continuing with power issues
Review
  Basic power issues
  Power Integrity
Discuss
  Battery selection
  DC converter options
Today…

## Slide 3: Review: Basic power issues
Electric power is the rate at which electric energy is transferred by an electric circuit.
  We often look at average power on different time scales depending on what we are wanting to know.
  Need to remember that lower power isn’t always the same as lower energy
    especially if the lower-power solution takes significantly longer

## Slide 4: Review: Power integrity (1/2)
Processors and other ICs have varying current demands
  Sometimes at frequencies much greater than the device itself runs at
    Why?
  So the power/ground inputs need to be able to deal with that.
    Basically we want those wires to be ideal and just supply how ever much or little current we need.
  If the current can’t be supplied correctly, we’ll get voltage droops.
How much power noise can we accept?
  Depends on the part (read the spec).
    If it can run from 3.5V to 5.5V we just need to insure it stays in that range.
  So we need to make sure that given the current, we don’t end up out of the voltage range.
Basically need to insure that we don’t drop too much voltage over the wires that are supplying the power!

## Slide 5: Review: Power integrity (2/2)
* http://www.n4iqt.com/BillRiley/multi/esr-and-bypass-caps.pdf provides a very nice overview of the topic and how to address it.
So we need the impedance of the wires to be low.
  Because the ICs operate at a wide variety of frequencies, we need to consider all of them.
  The wires themselves have a lot of inductance, so a lot of impedance at high frequencies.
    Need to counter this by adding capacitors.
Problem is that the caps have parasitic inductance and resistance.
  So they don’t help as well as you’d like
  But more in parallel is good.
  Each cap will help with different frequency ranges.
We also can get a small but low-parasitic cap out of the power/ground plane.
Finally we should consider anti-resonance*.

## Slide 6: Review-ish: Didn’t actually do last time
Why was 0.01 chosen as the target impedance?
  I flubbed this last time
Answer:
  If you can’t have more than a .1V ripple and you are pulling 10 Amps you need your impedance to be below .01 Ohms
    (V=IR so R=V/I)

## Slide 7: On to Batteries

## Slide 8: Outline
Introduction
  What is a battery?
  What characteristics do we care about?
  Define some terms.
Look in depth at a few battery types
Large parts of this section on batteries come from Alexander Cheng, Bob Bergen & Chris Burright

## Slide 9: Background: What is a battery?
  Voltaic Cells
    Two "half cells" connected in series by a conductive electrolyte containing anions and cations.
    One half cell contains the anode, which anions from the electrolyte migrate to. The other the cathode, which cations migrate to.
  Redox Reaction
    Anions at anode are oxidized
      removes electrons
    Cations at cathode are reduced
      adds electrons
  Creates an electrical current as electrons move.
Image from wikipedia
3

## Slide 10: What do we care about?
When picking batteries there are a number of characteristics to be aware of including:
  Voltage
  Max current
  Energy
  Results of mechanical failure
  Energy loss while idle
You have a lot of options because
  Many different battery types (Alkaline, LiPo, etc.)
  Different topologies (ways to connect the cells together)

## Slide 11: Lots of terms
  Capacity
    The amount of electric charge it can store, typically measured in mAh
  Charge Density
    Charge/Volume, measured in mWh/cm^3 or mWh/kg
  Charge Limit
    The maximum voltage the battery can produce under ideal conditions
  Primary Cells
    Non-rechargeable (disposable) batteries
  Secondary Cells
    Rechargeable batteries
  Lifetime
    Primary Cells - "self discharge", how long the battery lasts when not in use.
    Secondary Cells - recharge limits
  Cycle Life
    The number of charge cycles until battery can no longer reach 80% maximum charge

## Slide 12: Let’s look at “capacity”
Generally measured in mAh*, this tells us how much energy we can expect to get out of the device before it runs down.
  The problem is, we get less total energy the more quickly we drain the battery.
  Called “Peukert Effect”
    Actual capacity is dependent on the current draw.
      The faster you draw the current, the less you have total.
    Often irrelevant if just driving a microcontroller, but if have motors etc. it can be a big deal.
* While this unit isn’t really a measure of energy, it would be if voltage were fixed (which it more-or-less is)

## Slide 13: Peukert Effect
Image from http://www.vonwentzel.net/Battery/00.Glossary/

## Slide 14: Alkaline Battery
  Primary Battery
    Disposable
  Most common "off the shelf" battery
  Accounts for over 80% of manufactured batteries in the U.S.
  Over 10 billion individual units produced worldwide
Image from Wikipedia
9

## Slide 15: Lithium-Ion Polymer Battery
  Common abreviations:
    Li-poly, Li-Pol, Li-Po, LIP, PLI or LiP
  Secondary cell batteries
  Typically contain multiple cells in parallel
    Used to increase discharge current capacity
    Can cause charging difficulties
      Cells must be balanced for safe charging
12

## Slide 16: Lithium-Ion Polymer - Chemistry
  Sony's original lithium-ion battery used coke for the anode
    Coke was a by-product of the coal industry
  Modern lithium-ions began using graphite for the anode in about 1997
    Provides a flatter discharge curve
  Material combinations have been tested for the anode
    Tradeoffs are application dependent
14

## Slide 17: Lead Acid Battery
  Invented in 1859 by Gaston Plante
  Oldest rechargeable battery type
  Low energy to weight ratio
  Low energy to volume ratio
  Can supply high surge currents and hence high power to weight ratio
  The U.S. produces nearly 99 million wet-cell lead-acid batteries each year
16

## Slide 18: Lead Acid - Types
Lead Acid Battery Constructs:
  Flooded Cell (Wet Cell)
  Valve Regulated Lead Acid (VRLA)
    Gel
    Absorbed Glass Mat (AGM)
Lead Acid Battery Types:
  Starting Battery
  Deep Cycle Battery
  Marine Cycle
18

## Slide 19: Comparisons

## Slide 20: Electrical Properties - Capacity
  Alkaline
  Li-Po
    Typically 1100-1500 mAh per cell
    Like most Li-Ion a single battery contains multiple cells
  Lead-Acid
    Varies by size and type
    Car batteries are usually 50 Ah
20

## Slide 21: Electrical Properties - Current
  Alkaline
    Dependent on the size of the battery
    Rule of thumb:
      AA - 700mA max, 50mA typical
  Li-Po
    Can drive large currents
      Batteries rated for 1000mAh at 100mA draw can typically supply up to 1.5A, 15x their rated current
        This applies no matter the capacity or current draw ratings
    Connected in parallel to increase current rates
  Lead-Acid
    Can produce up to 500 amps if shorted
21

## Slide 22: Electrical Properties - Charge Density
  Alkaline
    Much higher than other "off the shelf" battery types
    Common cells typically 110 Wh/kg
  Li-Po
    100-180 Wh/kg
  Lead-Acid
    30-50 Wh/kg
22

## Slide 23: Cost
  Alkaline
    Very low cost to produce
      $0.19/Wh
    Most of the cost is placed on the consumer
  Li-Po
    Varies with chemical composition
      ~$0.47/Wh
    Cheaper than traditional Li-Ion
  Lead Acid
    $0.20/Wh
      Relatively cheap for high voltage applications
      Expensive for a full battery
24

## Slide 24: Hazards - Leaks
  Alkaline
    Cells may rupture and leak potassium hydroxide
      This will corrode the battery and the device
      May cause respiratory, eye, and skin irritation
  Li-Po
    Unlikely to leak because of solid internals
  Lead Acid
    Cells may rupture or be punctured
      Wet cells will leak strong sulfuric acid
25

## Slide 25: Hazards - Explosions/Fires
  Alkaline
    Unlikely to explode or catch fire
  Li-Po
    May explode or catch fire if mishandled
      Charging/Discharging too quickly builds heat
      Damaged cells are prone to explosions
  Lead Acid
    Electrolysis in flooded cells occurs when overcharge
      Produces hydrogen and oxygen gases which may explode if ignited
    VRLA does not contain liquid electrolytes
lithium-ion fire (http://www.gazettetimes.com/news/local/article_803a17e6-afd8-11e0-bedd-001cc4c03286.html)

## Slide 26: Hazards - Environmental Concerns
  Alkaline
    Ends up in landfills after one use
    Potassium hydroxide can corrode objects it touches
  Li-Po
    No major recycling programs in place currently
    Polymer requires strong chemicals and a lot of energy to produce
  Lead Acid
    Lead is a toxic metal
    97% of the lead is recycled
27

## Slide 27: Alkaline Battery Review
  Pros
    Disposable
    Cheap to produce, easy to obtain
    Maintenance-free
  Cons
    Non-rechargeable
    Moderate charge density
    Relatively low current drain limits
    Must be justifiable to the user
  Applications
    Household and mobile electronics
    Children's Toys
    Must be low current to justify disposable costs
    Low up-front costs
28

## Slide 28: Lithium-Ion Polymer - Review
  Pros:
    High energy density
    Relatively low self-discharge
    Low maintenance
      No periodic discharge is needed
      No memory
  Cons:
    Requires protection circuit to limit voltage and current
    Subject to aging, even if not in use
    Transportation regulations for shipping in large quantities
  Applications
    Lightweight portable electronic devices
      Cell phones, GPS, laptops, etc.
    Radio controlled model planes/cars
29

## Slide 29: Lead Acid - Review
  Pros
    Relatively cheap
    Long lifespan
    Able to provide extreme currents (500A+)
  Cons
    Heavy
    Large physical size
    Some models require periodic maintenance
  Applications
    Vehicle batteries
    Energy storage
      Off-the-grid systems
      Back up power supply
      Renewable energy systems
        Solar, wind, etc.
    Long term remote energy supply
30

## Slide 30: Example Situations
  Battery powered flashlight
    Must be compact and lightweight
    Needs to be cheap up front
    Batteries should be replaceable vs rechargeable
    Battery needs to have a long shelf life
  MP3 Player
    Must be compact and lightweight
    Expensive product can incorporate a higher battery cost
    Must be rechargeable
    Should recharge quickly
    Needs to have large energy capacity
    Must last 500+ recharge cycles without maintenance

## Slide 31: DC converters

## Slide 32: Outline
What are DC converters?
Linear regulators
  LDOs
Switching converters
Large parts of this section on converters come from Eric Lin

## Slide 33: What are DC converters?
DC converters convert one DC voltage level to another.
  Very commonly on PCBs
    Often have USB or battery power
    But might need 1.8V, 3.3V, 5V, 12V and -12V all on the same board.
  On-PCB converters allow us to do that
Images from http://itpedia.nyu.edu/wiki/File:V_reg_7805.jpg, http://www.electronics-lab.com/blog/wp-content/uploads/2007/10/p1000255.JPG

## Slide 34: Different types of DC converters
Linear converters
Switching converters
Simpler to design
Low-noise output for noise-sensitive applications
Can only drop voltage
  And in fact must drop it by some minimum amount
  The larger the voltage drop the less power efficient the converter is
Can be significantly more complex to design
  Worth avoiding for this class unless you have to do it.
Can drop voltage or increase voltage
  “buck” and “boost” respectively
Generally very power efficient
  75% to 98% is normal

## Slide 35: Characteristics of DC Converters
To better understand how to pick a converter we will go over the following characteristics seen in all DC converters
  Power wasted (as heat)
  Quiescent current,
    The leakage current that occurs regardless of operation.
  Power supply rejection ratio (PSRR)
    The ability to reject output noise at different frequency
  External capacitors and equivalent series resistance(ESR)
    Output noise filter that helps keeping the signal clean
These characteristics are what people generally look for when selecting converters, but they’re not by any means the only characteristics that matter.

## Slide 36: 1. Power Wasted (as Heat)
Linear converters waste power = (Vin– Vout)*Iload
  Example
    12 V battery supplying 5V to each device
      Microcontroller that draws 5mA
      Ultrasonic rangefinder that draws 50mA
    Use LM7805 (linear regulator) to drop 12V to 5V
    Power wasted = (12V – 5V) * (0.050A + 0.005A) = 0.385W
      Which is actually more than the power consumed!
      Is this acceptable?
        Hope so, because the alternative (switching converter) is a lot more difficult.
Switchers generally waste a more-or-less fixed percent
  Say 15% or so…
http://www.dimensionengineering.com/info/switching-regulators is the source for this example. They go into more detail on their site.

## Slide 37
In general…
  All have quiescent current (, which is different in each IC
    is affected by the input and temperature the device is operating at.
    Will drain battery so choose carefully when picking converters!
For this device, IQ is huge.
  Designed to move 1A.
LM7805 during operation
2. Quiescent current,
Diagrams from http://www.fairchildsemi.com/ds/LM/LM7805.pdf

## Slide 38: 3. Noise
PSRR indicates how well the supply deals with noise.
  Recall we rely on the VRM (voltage
  regulation module) to keep noise down at low frequencies.
  We don’t want noise on the output
  You can determine how well a linear converter handle noise by its PSRR
    PSRR is used to describe the amount of noise rejected by a particular device
  What does PSRR mean for noise rejection?
    Take 40dB @100kHz and 1V input, so
    Meaning for every 1V there may be 10 superimposed on the output
    70dB @ 10KHz is , so 3% of the noise at 100KHz!
  PSSR performance is crucial for noise sensitive operation
Typical PSRR profile for an LDO, 40dB @ 100kHz
Graph from digikey http://www.digikey.com/us/en/techzone/power/resources/articles/hybrid-power-supplies-noise-free-voltages.html
Notes: PSRR is the signal to noise ratio on the output and noise could be white noise or anything else

## Slide 39: 4. Caps and ESR.
What else would we have to look at regarding noise?
  Capacitors!
    Each converter requires at least a and sometimes a to reduce noise in the system
      Will be specified in datasheets
      Capacitors size generally needed from smallest to largest:
        General linear converters -> LDOs -> switching converters
min 22
min 22
LDO LM2940
Linear LM7805
Diagrams from http://www.fairchildsemi.com/ds/LM/LM7805.pdf and http://www.ti.com/lit/ds/symlink/lm2940-n.pdf

## Slide 40: 4. Caps and ESR.
Capacitors aren’t the only thing that will determine stability
  Sometime an operation demands higher and leaves the safe-operating-area (SOA) causing instability as well
    So in addition to the capacitors, equivalent series resistance (ESR) comes into play
    Like everything else, the capacitor and its ESR will be specified in each IC’s datasheet
    There’s also more than just ESR that affects the stability as well for varied and is discussed more in the link below
    http://www.bcae1.com/switchingpowersupplydesign/datasheets/ldoregulatorstabilityinfoslva115.pdf

## Slide 41: 4. Caps and ESR
So let’s take a look at an example of stability/instability with a changing
  Note the amount of noise in the top waveform ( as changes with the presence of ESR
Load transient with ceramic capacitor and ESR
Load transient with ceramic capacitor

## Slide 42: Quick look at the options
Linear converter
  LDO
Switching converter
  Buck
  Boost
  Buck-Boost

## Slide 43: Linear Converters
Now let’s look at linear converters and its LDO variety
In general linear converters…
  Acts like a variable resistor
  Drop voltage by heat dissipation through the network of resistors
  Often have a fairly high minimum voltage drop.
    If you want to drop less, need a specific type of linear converters
      “low-drop out” or LDO
LM7805 Linear Voltage Regulator Schematic
All this fits in the IC!
Diagrams from http://www.fairchildsemi.com/ds/LM/LM7805.pdf

## Slide 44: Linear Converters - LDO
What are low-dropout regulators(LDO)?
  LDOs are more complex linear regulators, using a transistor and error amplifier for negative feedback
  Larger capacitor is now needed
    Inherently, the capacitors will have equivalent series resistance that will also contribute to noise reduction. This will be discussed in later slides
  Also implemented as ICs like the other linear regulators
LP5900
Generic LDO schematic

## Slide 45: Switching Converters
Once you leave the realms of linear converters it gets more complex.
  Introducing common switching converters!
    All include a diode, transistor, inductor and a capacitor
Schematics are from http://www.nxp.com/documents/application_note/APPCHP2.pdf
Converters | General Topology | Application
Buck |  | Drop voltage
Boost |  | Increase voltage
Buck-boost(inverting) |  | Increase or decrease voltage and inverse polarity

## Slide 46: That’s all for today.
We’ll pick up details of these devices next time.