## Slide 1: EECS 498 Advanced Embedded Systems
Lecture 10:
Power review, Switching power supplies, Start on signal integrity

## Slide 2: Class stuff
Exam answers posted
Camera group hasn’t seen me yet
Sign up for design expo
  Dec 6th!
  Which groups haven’t?
Nov 8th is last day to order PCBs
Milestone 2 next Monday
  One page summary/memo of
    Where you are
    What you are behind on
    What you need help with
  Meeting as before

## Slide 3: EE review
Exam made it clear I needed to review some basics:
  V=IR
  P=I2R and P=VI
    What if I just have V and R?
  Review question
    What is the voltage drop across the resistor that has .1A flowing through it? The 10A resistor?
    How much power is lost in the bottom resistor?
0.1A
0.05Ω
10A
3.3V
12V
Notes: .1A+10A=10.1A*.05Ω=.505V, so we have a bit less than 2.8V!
10.1^2~=100 * 0.05=5Watts!

## Slide 4: Review: Power Distribution Network
Talked a lot about keeping the power supply voltage constant.
  Should think of situation as follows:
  If the processor drops 3.3V and uses 100mA, what is it’s effective resistance?
  If the power supply is 3.3V, the processor uses 100mA and the total resistance of the PDN (Power distribution network) is .01Ω, what voltage does the processor really see?
Input
PDN
Processor
Output
PDN

## Slide 5: Review: Power integrity (1/2)
Processors and other ICs have varying current demands
  Sometimes at frequencies much greater than the device itself runs at
    Why?
  So the power/ground inputs need to be able to deal with that.
    Basically we want those wires to be ideal and just supply how ever much or little current we need.
  If the current can’t be supplied correctly, we’ll get voltage droops.
How much power noise can we accept?
  Depends on the part (read the spec).
    If it can run from 3.5V to 5.5V we just need to insure it stays in that range.
  So we need to make sure that given the current, we don’t end up out of the voltage range.
Basically need to insure that we don’t drop too much voltage over the wires that are supplying the power!

## Slide 6: Review: Power integrity (2/2)
* http://www.n4iqt.com/BillRiley/multi/esr-and-bypass-caps.pdf provides a very nice overview of the topic and how to address it.
So we need the impedance of the wires to be low.
  Because the ICs operate at a wide variety of frequencies, we need to consider all of them.
  The wires themselves have a lot of inductance, so a lot of impedance at high frequencies.
    Need to counter this by adding capacitors.
Problem is that the caps have parasitic inductance and resistance.
  So they don’t help as well as you’d like
  But more in parallel is good.
  Each cap will help with different frequency ranges.
We also can get a small but low-parasitic cap out of the power/ground plane.
Finally we should consider anti-resonance*.

## Slide 7: Battery review: Lots of terms
  Capacity
    The amount of electric charge it can store, typically measured in mAh
  Charge Density
    Charge/Volume, measured in mWh/cm^3 or mWh/kg
  Charge Limit
    The maximum voltage the battery can produce under ideal conditions
  Primary Cells
    Non-rechargeable (disposable) batteries
  Secondary Cells
    Rechargeable batteries
  Lifetime
    Primary Cells - "self discharge", how long the battery lasts when not in use.
    Secondary Cells - recharge limits
  Cycle Life
    The number of charge cycles until battery can no longer reach 80% maximum charge

## Slide 8: Battery review: Peukert Effect
Image from http://www.vonwentzel.net/Battery/00.Glossary/

## Slide 9: But wait…
Peukert numbers are all over the map
  No one value for a given type of cell
    I’ve found lead-acid car batteries with values from 1.1 to 1.4 (huge variation)
    And it is generally agreed LA will have this value move depending on how you drain it.
      They hate constant draw, do high- current short draws well…
    Other batteries have their own properties…

## Slide 10: DC converters

## Slide 11: Outline
What are DC converters?
Linear regulators
  LDOs
Switching converters
Large parts of this section on converters come from Eric Lin

## Slide 12: What are DC converters?
DC converters convert one DC voltage level to another.
  Very commonly on PCBs
    Often have USB or battery power
    But might need 1.8V, 3.3V, 5V, 12V and -12V all on the same board.
  On-PCB converters allow us to do that
Images from http://itpedia.nyu.edu/wiki/File:V_reg_7805.jpg, http://www.electronics-lab.com/blog/wp-content/uploads/2007/10/p1000255.JPG

## Slide 13: Different types of DC converters
Linear converters
Switching converters
Simpler to design
Low-noise output for noise-sensitive applications
Can only drop voltage
  And in fact must drop it by some minimum amount
  The larger the voltage drop the less power efficient the converter is
Can be significantly more complex to design
  Worth avoiding for this class unless you have to do it.
Can drop voltage or increase voltage
  “buck” and “boost” respectively
Generally very power efficient
  75% to 98% is normal

## Slide 14: Characteristics of DC Converters
To better understand how to pick a converter we will go over the following characteristics seen in all DC converters
  Power wasted (as heat)
  Quiescent current,
    The leakage current that occurs regardless of operation.
  Power supply rejection ratio (PSRR)
    The ability to reject output noise at different frequency
  External capacitors and equivalent series resistance(ESR)
    Output noise filter that helps keeping the signal clean
These characteristics are what people generally look for when selecting converters, but they’re not by any means the only characteristics that matter.

## Slide 15: 1. Power Wasted (as Heat)
Linear converters waste power = (Vin– Vout)*Iload
  Example
    12 V battery supplying 5V to each device
      Microcontroller that draws 5mA
      Ultrasonic rangefinder that draws 50mA
    Use LM7805 (linear regulator) to drop 12V to 5V
    Power wasted = (12V – 5V) * (0.050A + 0.005A) = 0.385W
      Which is actually more than the power consumed!
      Is this acceptable?
        Hope so, because the alternative (switching converter) is a lot more difficult.
Switchers generally waste a more-or-less fixed percent
  Say 15% or so…
http://www.dimensionengineering.com/info/switching-regulators is the source for this example. They go into more detail on their site.

## Slide 16
In general…
  All have quiescent current (, which is different in each IC
    is affected by the input and temperature the device is operating at.
    Will drain battery so choose carefully when picking converters!
For this device, IQ is huge.
  Designed to move 1A.
LM7805 during operation
2. Quiescent current,
Diagrams from http://www.fairchildsemi.com/ds/LM/LM7805.pdf

## Slide 17: 3. Noise
PSRR indicates how well the supply deals with noise.
  Recall we rely on the VRM (voltage
  regulation module) to keep noise down at low frequencies.
  We don’t want noise on the output
  You can determine how well a linear converter handle noise by its PSRR
    PSRR is used to describe the amount of noise rejected by a particular device
  What does PSRR mean for noise rejection?
    Take 40dB @100kHz and 1V input, so
    Meaning for every 1V there may be 10 superimposed on the output
    70dB @ 10KHz is , so 3% of the noise at 100KHz!
  PSSR performance is crucial for noise sensitive operation
Typical PSRR profile for an LDO, 40dB @ 100kHz
Graph from digikey http://www.digikey.com/us/en/techzone/power/resources/articles/hybrid-power-supplies-noise-free-voltages.html
Notes: PSRR is the signal to noise ratio on the output and noise could be white noise or anything else

## Slide 18: 4. Caps and ESR.
What else would we have to look at regarding noise?
  Capacitors!
    Each converter requires at least a and sometimes a to reduce noise in the system
      Will be specified in datasheets
      Capacitors size generally needed from smallest to largest:
        General linear converters -> LDOs -> switching converters
min 22
min 22
LDO LM2940
Linear LM7805
Diagrams from http://www.fairchildsemi.com/ds/LM/LM7805.pdf and http://www.ti.com/lit/ds/symlink/lm2940-n.pdf

## Slide 19: 4. Caps and ESR.
Capacitors aren’t the only thing that will determine stability
  Sometime an operation demands higher and leaves the safe-operating-area (SOA) causing instability as well
    So in addition to the capacitors, equivalent series resistance (ESR) comes into play
    Like everything else, the capacitor and its ESR will be specified in each IC’s datasheet
    There’s also more than just ESR that affects the stability as well for varied and is discussed more in the link below
    http://www.bcae1.com/switchingpowersupplydesign/datasheets/ldoregulatorstabilityinfoslva115.pdf

## Slide 20: 4. Caps and ESR
So let’s take a look at an example of stability/instability with a changing
  Note the amount of noise in the top waveform ( as changes with the presence of ESR
Load transient with ceramic capacitor and ESR
Load transient with ceramic capacitor

## Slide 21: Quick look at the options
Linear converter
  LDO
Switching converter
  Buck
  Boost
  Buck-Boost

## Slide 22: Linear Converters
Now let’s look at linear converters and its LDO variety
In general linear converters…
  Acts like a variable resistor
  Drop voltage by heat dissipation through the network of resistors
  Often have a fairly high minimum voltage drop.
    If you want to drop less, need a specific type of linear converters
      “low-drop out” or LDO
LM7805 Linear Voltage Regulator Schematic
All this fits in the IC!
Diagrams from http://www.fairchildsemi.com/ds/LM/LM7805.pdf

## Slide 23: Linear Converters - LDO
What are low-dropout regulators(LDO)?
  LDOs are more complex linear regulators, using a transistor and error amplifier for negative feedback
  Larger capacitor is now needed
    Inherently, the capacitors will have equivalent series resistance that will also contribute to noise reduction. This will be discussed in later slides
  Also implemented as ICs like the other linear regulators
LP5900
Generic LDO schematic

## Slide 24: Switching Converters
Once you leave the realms of linear converters it gets more complex.
  Introducing common switching converters!
    All include a diode, transistor, inductor and a capacitor
Schematics are from http://www.nxp.com/documents/application_note/APPCHP2.pdf
Converters | General Topology | Application
Buck |  | Drop voltage
Boost |  | Increase voltage
Buck-boost(inverting) |  | Increase or decrease voltage and inverse polarity

## Slide 25: Functionality – Switching Converters
Common switching converters
  Converters now includes a transistor and diode used for switching and an inductor as energy storage.
    In general, a switching converters works by controlling the frequency and duty cycle that the transistor is operating at
  Similar to linear converters, most of the work is already done.
  Only have to pick IC with the right parameter and follow the datasheets given for appropriate inductors and capacitors.
Size of inductor in relation to the rest of the component
Example switching regulator from http://ycprojects.wordpress.com/

## Slide 26: Functionality – Switching Converters
Common switching converters
  Aside from the noble goal of making circuit analysis more complex () both the inductor and capacitor play important roles in switching converters.
    Capacitor
      Used to store energy due to the voltage applied thus maintaining a constant voltage
      Generally selected to limit ripple to the correct specification
    Inductors
      Similar to the capacitor, but an inductor is use to store energy due to current flow. This in turn maintain a constant current or is used to limit the rate of change of current flow.
      This will also determine the peak to peak current in the circuit which affects the transistor, diode and the “mode” the converter will operate at

## Slide 27: Functionality – Switching Converters
Common switching converters
  In addition to filtering and maintaining a constant output, inductors/capacitors will also have effect on the transient response. As you can see on the right, depending on the values of the inductor/capacitor the current flow and the transient response time will be different.
Example transient response of a buck converter
Blue: L= 40 C = 500
Red: L = 40 C = 2500
Black: L= 60 C= 500

## Slide 28: Functionality – Buck
Common switching converters
  To better describe the operation for switching converter let’s use the buck converter as an example
    Note the drive circuit, this is what the IC is
    For simplicity’s sake let’s disregard and , the internal resistance of the inductor and capacitor
    We will mainly focus on the effect switching on the current flow of the circuit and the stresses on the transistor and diode

## Slide 29: Functionality – Buck
Common switching converters - buck
  During operation, the buck converter functions differently depending on the switch
    On state
      Current flows through the transistor but reverse bias prevents current flow through the diode
      Inductor begins to charge and a smaller current becomes
    Off state
      Switch opens and the inductor starts discharging as the only power source
    This on-off state will determine the “mode” the converter operate in
Buck: switch on
Buck: switch off

## Slide 30: Functionality – Switching Converters
Common switching converters
  In switching converters, load current and voltage is largely determined by the operation of transistor switching
    The duty cycle of the switching will determine the mode each converter operate at various loads
      Continuous Mode
        The inductor current will never fall to zero when the switch is off
        Smaller current peak during operation
      Discontinuous Mode
        Inductor current will reach zero before the end of the full duty cycle
      Each mode has its advantages and disadvantages depending on the switching converters.
        In generally it’s how they change the frequency response.

## Slide 31: Functionality – Buck
  Continuous mode
  Discontinuous mode
Common switching converters
    Using buck converter as an example, you can see the pulses with a certain /. This is the duty cycle of the transistor switching
    When the transistor is on it also creates a reverse bias voltage () across the diode. With a large enough voltage the diode will “breakdown” !
Notes: Add cite

## Slide 32: Functionality – Buck
  Continuous mode
  Discontinuous mode
Common switching converters
    As the switch is on there is current flow through the transistor
      Current is a ramp because of the inductor
      High peak also creates more stress on the transistor

## Slide 33: Functionality – Buck
  Continuous mode
  Discontinuous mode
Common switching converters
    During the off time there is now forward bias current flowing through the diode from inductor discharging
    This is also when the inductor starts discharging so the current starts to ramp down

## Slide 34: Functionality – Buck
  Continuous mode
  Discontinuous mode
Common switching converters
    The output now has a ripple to it and not desirable for controlling the converter
      Instead of , so when the feedback happens the control can read a constant value
      From the feedback the switching duty cycle is changed to keep the converter in a particular state.

## Slide 35: Functionality – Buck
  Continuous mode
  Discontinuous mode
Common switching converters
    For buck converters we want to operate at continuous mode because only depends on the duty cycle which makes it easier to control
    There are many published paper that cover the subject, a good one is http://www.ti.com/lit/an/slva057/slva057.pdf

## Slide 36: Functionality – Boost
Common switching converters
  Boost(step-up)
  Looks similar to buck converter but the topology is different and has different on/off states
    On state
      Current flow through the transistor(least resistance) making the diode reverse bias and no
      Inductor is charged in the process
    Off state
      The energy discharged by the inductor is superimposed to the input, generating a higher output
Generic boost schematic
Boost: on state
Boost: off state
Schematics from http://en.wikipedia.org/wiki/Boost_converter

## Slide 37: Functionality – Switching Converters
  Continuous mode
  Discontinuous mode
Common switching converters - Boost
    From the timing diagram you can see this is very similar to the buck timing diagram with a difference in that only affects directly when the switch is off
    Similar to buck, in continuous mode the output is control by the duty cycle.
      But unfortunately, boost favor discontinuous mode, in continuous mode there is a complex second order characteristic in noise. Discontinuous mode removes the inductance noise, producing simpler response to compensate and control
Schematics from http://en.wikipedia.org/wiki/Boost_converter

## Slide 38: Functionality – Switching Converters
Common switching converters
  Buck-boost(inverting)
    The baby of buck and boost…
    On state
      Diode is reverse biased and the inductor is charged but input and output is isolated from each other
        Creates more stress on the diode!
      is now the charged from off state but different polarity
    Off state
      Inductor voltage reverses, passing energy to the capacitor and load through forward biased diode
    Due to the characteristics of boost, buck-boost suffers the same problem. Therefore a discontinuous mode is favored
Generic buck- boost schematic
Buck-boost: on state
Buck-boost: off state
Schematics from http://en.wikipedia.org/wiki/Buck%E2%80%93boost_converter

## Slide 39: Functionality – Switching Converters
To give you a better idea of how duty cycle affect the output of each converter in continuous mode refer to the table below
  Each duty cycle equation is equal to the ratio of
  In discontinuous mode these equations are no longer true, but we will not discuss them here and they can also be found online
  More information on each of the switching converter can be found at http://www.nxp.com/documents/application_note/APPCHP2.pdf http://ecee.colorado.edu/copec/book/slides/Ch5slide.pdf http://www.ti.com/lit/an/slva057/slva057.pdf
Converters | Duty cycle
Buck | 
Boost | 
Buck-boost(inverting) | 
Converters | Duty cycle
Buck | 
Boost | 
Buck-boost(inverting) | 

## Slide 40: Picking converters
Hopefully at this point you can start to see how much more complicated a switching converter is relative to a linear converter
  Every change made to the capacitor, inductor, transistor or diode will have an significant effect in not only the efficiency of each converter but also the life and way they operate
  Fortunately it won’t be the end of the world if you decide to use switching converters
    Using mic2168a, a controller for buck converter, as example. We can see not only do they provide information on the controller but also the external components needed for proper functionality (9pages!).
  ON semiconductor also provide a detailed published paper on both linear and switching regulator, covering the theory and design consideration needed.

## Slide 41: Picking converters
For those who aren’t as interested in all the technical details behind all this can refer to TI’s power management portal.
You can just enter the parameters and TI will come up with recommendation
Other companies also offer similar things so you’re not stuck with only TI
  Try Micrel, Freescale or other brands as needed.

## Slide 42: Back to review:
Return paths.
  Ground isn’t ground.
    This is an important rule.
  Back to review question
    What is the voltage drop across the resistor that has .1A flowing through it? The 10A resistor?
    How much power is lost in the bottom resistor?
  How does this relate to anything?
0.1A
0.05Ω
10A
3.3V
12V